Wastewater Treatment Plants and Discharge Information

Watershed boundaries were used as a tool to examine the number of wastewater treatment plants or sewage discharges that possibly impact the beach sites used in this study.  Only wastewater treatment plants or sewage discharges within the same watershed boundaries as the study site were included.  Because the study sites involve coastal areas in the Great Lakes region, watersheds surrounding the sites generally include a river basin and a lake watershed.  For example, West Beach, Washington Park and Silver Beach were contained within the Lake Michigan Watershed as well as the corresponding River Basins such as the Little Calumet-Galien and the St. Joseph Watersheds respectively.

The following tables for each study site describe the characteristics of wastewater treatment plants contained in the watersheds of interest.  The receiving stream column indicates where the water discharge is located.  Only wastewater treatment plants (WWTP) or sewage effluent discharge locations that provide a point source discharging into a receiving stream, or one of its tributaries, in the beach watershed are included.  In addition to information obtained from the National Pollutant Discharge Elimination System (NPDES) system, other information was obtained from websites describing population served (http://cfpub.epa.gov/cwns/population.cfm) and beach areas including maps and watershed boundaries (http://igs.indiana.edu/arcims/statewide/index.html; http://nhd.usgs.gov/).  Additional information came from NPDES Fact Sheets, permit document data, and verbal correspondence with plant operators.  Information used to identify areas of impact was available through the EPA Enviromapper National Wetlands Inventory.  WWTPs using the chlorine disinfection with dechlorination and ultraviolet processes, generally only apply it seasonally (April to October).

### West Beach

West Beach is positioned just west of Burns Ditch and on Lake Michigan.  The watersheds that contain both the study site and Burns Ditch, which discharges into Lake Michigan, are the Little Calumet-Galien and the Lake Michigan Watersheds.  Within these watersheds there are seven identified sewage discharges into the Burns Ditch or one of its tributaries.  Three of the sewage discharges are WWTPs that are ranked as Major Dischargers.  The three closest WWTPs serve more than 66,000 customers (see Figure A1).

Table A1: West Beach Wastewater Treatment Plants

| NPDES Identification Number | Receiving Stream | Flow Rate* | Major Dischargers | Serving Population | Treatment and Process |
| --- | --- | --- | --- | --- | --- |
| 1-IN0024368 | Burns | 4 | M | 29,824 | Secondary treatment Ultraviolet disinfection |
| 2-INL022578 | East Branch Little Calumet | 3 | M | 10,488 | Secondary treatment Chlorine disinfection with dechlorination |
| 3-IN0024660 | Salt Creek | 6 |  | 26,151 | Secondary treatment Chlorine disinfection with dechlorination |
| 4-IN0058475 | Tributary of Clark Ditch | .35 | -- | -- | Secondary treatment Ultraviolet disinfection |
| 5-IN0058378 | Deep River | .03 | -- | -- | Septic tanks Recirculating sand filters Chlorine disinfection with dechlorination |
| 6-IN0025763 | LM/CLMT-BRNS | 4 | M | -- | Secondary treatment Chlorine disinfection with dechlorination |
| 7-INU31089 | Kaiser Creek | -- | -- | -- | Primary treatment No disinfection |

*	Million gallons per day

### Huntington Beach

Huntington Beach is located in the Black-Rocky Watershed with ten identified sewage discharge locations.  Three of the sewage discharges empty directly into Lake Erie and these include Avon Lake (west of the study site), and the Rocky River and Westerly plants which are situated to the east.  The Rocky River or one of its tributaries is the receiving stream for all other identified sewage discharges.  Four of these sewage discharges are WWTPs that are major dischargers.  The three WWTPs located on Lake Erie serve over 38,000 persons while the seven WWTPs that surround the Rocky River serve in excess of 180,000 persons (see Figure A2).

Table A2: Huntington Beach Wastewater Treatment Plants

| NPDES Identification Number | Receiving Stream | Flow Rate* | Major Discharger | Serving Population | Treatment and Process |
| --- | --- | --- | --- | --- | --- |
| 1-OH0030503 | Lake Erie | 22 | -- | 20,735 | Secondary treatment Chlorine disinfection with dechlorination |
| 2-OH0026018 | Lake Erie Lakewood | 18 | M | 56,646 | Secondary treatment Chlorine disinfection with dechlorination |
| 3-OH0024660 | Lake Erie Westerly | 50 | M | 1 | Secondary treatment Chlorine disinfection with dechlorination |
| 4-OH0026778 | Rocky River | 7.5 | M | 34,113 | Secondary treatment Chlorine disinfection with dechlorination |
| 5-OH0027570 | Baldwin Creek Two facilities | 1.0 & .844 | -- | 12,000 & 5,800 | Tertiary treatment Chlorine disinfection with dechlorination |
| 6-OH0026808 | Baldwin Creek | .69 | -- | 4,800 | Primary treatment Chlorine disinfection with dechlorination |
| 7-OH0026794 | Rocky River | 3.3 | -- | 14,000 | Tertiary treatment Ultraviolet disinfection |
| 8-OH0044466 | Ridgeway Ditch | .17 | -- | 58,000 | Secondary treatment Chlorine disinfection with dechlorination |
| 9-OH0026166 | West Branch Rocky | .01 | -- | 62 | Secondary treatment Chlorine disinfection with dechlorination |
| 10-OH0023981 | Lake Erie-Avon Lake | 6.5 | M | 18,145 | Secondary treatment Ultraviolet disinfection |

*	Million gallons per day

### Washington Park

Washington Park Beach is on the northern border of Indiana.  Trail Creek enters Lake Michigan directly to the east of the beach study site. This creek is part of the Michigan City Sanitary District WWTP which is categorized as a major discharger and serves over 38,000 persons (see Figure A3).

Table A3: Washington Park Wastewater Treatment Plants

| NPDES Identification Number | Receiving Stream | Flow Rate* | Major Discharger | Serving Population | Treatment and Process |
| --- | --- | --- | --- | --- | --- |
| 1-IN0023752 | Trail Creek | 12 | M | 38,486 | Secondary treatment Chlorine disinfection with dechlorination |

*	Million gallons per day

### Silver Beach

Silver Beach is located just south of where the St. Joseph River empties into the eastern shore of Lake Michigan.  It is in the St. Joseph and Lake Michigan watersheds.  The St. Joseph River extends from the lake through the center of Berrien County to its southern innermost border. All of the sewage discharges included in the table below have St. Joseph River, or one of its tributaries, as a receiving stream.  Two of the sewage discharges are WWTPs that are categorized as major dischargers and the four WWTPs located directly on the St. Joseph River serve more than 58,000 persons (see Figure A4).

Table A4: Silver Beach Wastewater Treatment Plants

| NPDES Identification Number | Receiving Stream | Flow Rate* | Major Discharger | Serving Population | Treatment and Process |
| --- | --- | --- | --- | --- | --- |
| 1-MI0022322 | St. Joseph River | 15 | M | 38,614 | Secondary treatment Chlorine disinfection with dechlorination |
| 2-MI00G570204 | St. Joseph River | 1 | -- | 1,954 | No pretreatment. Chlorine disinfection with dechlorination |
| 3-MI0022489 | St. Joseph River | 2 | -- | 4,992 | Secondary treatment Chlorine disinfection with dechlorination |
| 4-MI0023701 | St. Joseph River | 6 | -- | 12,458 | Secondary treatment Chlorine disinfection with dechlorination |
| 5-MIG00580309 | Hickory Creek | 10 | -- | -- | No information |
| 6-MIG00570105 | Paw Paw River | 0.5 | -- | -- | No information |
| 7-MI0023779 | Paw Paw River | 2 | M | 0 | Secondary treatment Chlorine disinfection with dechlorination |

*	Million gallons per day

Figure A1: West Beach wastewater treatment plants

Figure A2: Huntington Beach wastewater treatment plants

Figure A3: Washington Park wastewater treatment plants

Figure A4: Silver Beach wastewater treatment plants