unit ControlAlgorithm;

*******************************************************************************

This unit contains the relevant code for the control algorithm mentioned in the paper in Anesthesiology. It is called by the main program every time the main program receives a new BIS value when in automatic control mode. The code in this unit was adapted from code included in a program written for an AEP-based closed loop anesthesia system. The main BIS-based closed loop anesthesia program, and the adaptation of the control algorithm code was written by Dr A Absalom of Glasgow University with Borland Delphi 2 (Inprise, Scotts Valley, CA, USA).

Only the code specific to the control algorithm itself is included, although other functions used in the program are listed. The reader is reminded that automatic control of anesthesia is not standard clinical practise, and can and should only occur under closely controlled conditions under the supervision or direct control of experts in the field. No part of the code listed below may be copied, or duplicated for this use. The authors of the paper, and their employers cannot be held liable for any consequences of the use of closed loop control of anesthesia by anybody else. Should any person or organisation attempt to use closed loop control of anesthesia they do so entirely at their own risk.

*******************************************************************************

interface

uses

Type

TrgtBloodPropArray = array[1..3] of Single;

TControlAlg = class(TObject)

private

Procedure InitializeControlVars;

Procedure SetMaxTrgtProp(MaxProp : Integer);

Property AsaStatus: Integer Read FAsaStatus Write FAsaStatus;

Property AutoMode: Integer Read FAutoMode Write FAutoMode;

public

Function CalcTrgtPropofol(BISActual:Integer;

CurrentBloodProp:single):single;

Procedure SetMinTrgtProp(MinProp : Integer);

Procedure SetVariance(Variance : Integer);

procedure SetBISTrgt(Target: Integer);

constructor Create(aowner: TObject; ASA: Integer);

destructor Free;

published

Property MaxTrgtProp: Integer Read FMaxTrgtProp Write SetMaxTrgtProp;

Property MinTrgtProp: Integer Read FMinTrgtProp Write SetMinTrgtProp;

Property BISVar: Integer Read FBISVar Write SetVariance;

property BISTrgt: Integer Read FBISTrgt Write SetBISTrgt;

end;

const

SecsPerDay = 60*60*24;

// Automatic control constants

MntTrgtPropEmerg: array[1..3] of real;

DeltaTrgtPropMax: array[1..3] of real;

MNTminProp;

Kp: array[1..3] of real;

Ki: array[1..3] of real;

AutoCutBack: array[1..3] of real;

var

NewBIS, Error, ErrorOld: Integer;

TrgtBloodProp, CurrentBloodProp, SumDeltaTrgtProp, DeltaTrgtProp: Single;

FirstLoop, TrgtPropChanged: Boolean;

AutoTimeBase, AutoTimer, TimeSinceLastChange, TimeOfLastChange: TDateTime;

TimePrevBIS, TimeCurrBIS: TDateTime;

implementation

Function TControlAlg.CalcTrgtPropofol(BISActual: Integer;

CurrentBloodProp:single):single;

begin

// Initialise some settings

if Firstloop = True then

begin

TrgtBloodProp := CurrentBloodProp;

FirstLoop := False;

AutoTimeBase := Time;

AutoTimer := 1/SecsPerDay;

TimePrevBIS := Time;

end;

TimePrevBIS := TimeCurrBIS;

TimeCurrBIS := Time;

TimeSinceLastChange := Time - TimeOfLastChange;

// Calculate the error

Error := BISActual - BISTrgt;

// Calculate the Propofol target adjustment from this single error

DeltaTrgtProp := Kp[ASAStatus] * (Error - ErrorOld) +

Kp[ASAStatus] * (Ki[ASAStatus] * ((TimeCurrBIS-TimePrevBIS)*SecsPerDay) * Error);

// Check if there actual blood propofol is close to the previous target

// and if the error > BISVar (allowable error)

if ((CurrentBloodProp >= TrgtBloodProp-0.5) and (CurrentBloodProp<=TrgtBloodProp+0.5) and (TrgtBloodProp>=3))

or ((CurrentBloodProp>=TrgtBloodProp-1) and (CurrentBloodProp<=TrgtBloodProp+1) and (TrgtBloodProp<3) and (TrgtBloodProp>2.0))

or ((CurrentBloodProp>=TrgtBloodProp-2) and (CurrentBloodProp<=TrgtBloodProp+2) and (TrgtBloodProp<=2))

or (BISActual > BISTrgt + BISVar)

then

begin

// Limit the interim propofol concentration adjustment to the preset maximum

// change

if DeltaTrgtProp > DeltaTrgtPropMax[ASAStatus] then

DeltaTrgtProp := DeltaTrgtPropMax[ASAStatus];

// Add the above adjustment to the previous ones from the current 30s epoch

SumDeltaTrgtProp:=SumDeltaTrgtProp+DeltaTrgtProp;

// Calculate time since last propofol target change

if (TimeSinceLastChange >= (30/SecsPerDay)) then

begin

// If it is >= 30 sec since the last propofol target change then

// change the target to the current concentration + SumDeltaTrgtProp

TrgtBloodProp := TrgtBloodProp + SumDeltaTrgtProp

// and reset time and SumDeltaTrgtProp values

TimeOfLastChange := Time;

SumDeltaTrgtProp:=0;

end;

end;

// Store the current error value as the old one

ErrorOld := Error;

// Calculate how long since last automatic target reduction

AutoTimer := Time - AutoTimeBase;

// Make a small reduction to the target every 180 sec

if (AutoTimer > (180/SecsPerDay)) then

begin

AutoTimeBase := Time;

AutoTimer := 0;

TrgtBloodProp := TrgtBloodProp - AutoCutBack[ASAStatus];

end;

// If propofol target is less than the minimum, make it the minimum

if TrgtBloodProp < MinTrgtProp then

begin

TimeOfLastChange := Time;

TrgtBloodProp := MinTrgtProp;

end;

// If the propofol target is greater than the maximum, set it at the maximum

if TrgtBloodProp > MaxTrgtProp then

begin

TimeOfLastChange := Time;

TrgtBloodProp := MaxTrgtProp;

end;

// Round the target value to one figure after the decimal point

CalcTrgtPropofol := round(TrgtBloodProp*10)/10;

end;

constructor TControlAlg.Create(aOwner: TObject; ASA: Integer);

destructor TControlAlg.Free;

Procedure TControlAlg.InitializeControlVars;

Procedure TControlAlg.SetBISTrgt(Target: Integer);

Procedure TControlAlg.SetMaxTrgtProp(MaxProp: Integer);

Procedure TControlAlg.SetMinTrgtProp(MinProp: Integer);

Procedure TControlAlg.SetVariance(Variance: Integer);

end.