Characteristics of the Ventilatory Status of Patients with Tension Pneumothorax in Included Case Reports/Series.

| Characteristic – No. (%) | All Cases (n=183) | Cases Satisfying Published Tension PTX Definition* (n=103) |
| --- | --- | --- |
| Breathing unassisted | 86 (47.0) | 33 (32.0) |
| Breathing spontaneously without any type of indwelling airway device | 85/86 (98.8) | 32/33 (97.0) |
| Breathing spontaneously through an endotracheal tube and T-piece without any added positive pressure | 1/86 (1.2) | 1/33 (3.0) |
| Assisted ventilation | 97 (53.0) | 70 (68.0) |
| Type of assisted ventilation |  |  |
| Endotracheal intubation or tracheostomy with mechanical ventilation | 66/97 (68.0) | 45/70 (64.3) |
| Peak airway pressure, median (IQR), cm H2O | 30 (23-37.5) | 30 (23-36) |
| Studies reporting peak airway pressure | 21/66 (31.8) | 17/45 (37.8) |
| Positive end-expiratory pressure, median, cm H2O | 5.5 (5-10) | 5 (5-8) |
| Studies reporting positive end-expiratory pressure | 18/66 (27.3) | 13/45 (28.9) |
| Endotracheal intubation with manual ventilation | 10/97 (10.3) | 8/70 (11.4) |
| Endotracheal intubation with manual or mechanical ventilation (unclear which) | 6/97 (6.2) | 4/70 (5.7) |
| Bag mask ventilation without endotracheal intubation | 1/97 (1.0) | 1/70 (1.4) |
| Jet ventilation via an airway exchange or other type of catheter | 8/97 (8.3) | 7/70 (10.0) |
| Jet ventilation driving pressure, median, PSI | 50 (15-50) | 39.5 (15-50) |
| Studies reporting driving pressure | 7/8 (87.5) | 6/7 (85.7) |
| Other† | 6/97 (6.2) | 5/70 (7.1) |

Where IQR indicates interquartile range; PSI, pounds per square inch; and PTX, pneumothorax.

*According to this definition, a tension PTX is one that results in significant respiratory or hemodynamic compromise that reverses (or at least significantly improves) on thoracic decompression alone.

†Other types of assisted ventilation included endotracheal intubation with the tube attached to a self-inflating bag-valve device (1 case), endotracheal inubation with the ventilator tubing connected to the ventilator-mounted switch valve post usually occupied by the reservoir bag (2 cases), connection of the tube for the oxygen mask to the endotracheal tube in error in an intubated patient (1 case), endotracheal intubation with erroneous connection from the ventilator to the gas machine (1 case), and endotracheal intubation and ventilation with a hand resuscitator (1 case).